## Slide 1
Lecture 3: MIPS Instruction Set
Today’s topic:
  MIPS instructions

## Slide 2
Instruction Set
Understanding the language of the hardware is key to understanding
the hardware/software interface
A program (in say, C) is compiled into an executable that is composed
of machine instructions – this executable must also run on future
machines – for example, each Intel processor reads in the same x86
instructions, but each processor handles instructions differently
Java programs are converted into portable bytecode that is converted
into machine instructions during execution (just-in-time compilation)
What are important design principles when defining the instruction
set architecture (ISA)?

## Slide 3
Instruction Set
Important design principles when defining the
instruction set architecture (ISA):
  keep the hardware simple – the chip must only
  implement basic primitives and run fast
  keep the instructions regular – simplifies the
  decoding/scheduling of instructions
  We will later discuss RISC vs CISC

## Slide 4
A Basic MIPS Instruction
C code: a = b + c ;
Assembly code: (human-friendly machine instructions)
add a, b, c # a is the sum of b and c
Machine code: (hardware-friendly machine instructions)
00000010001100100100000000100000
Translate the following C code into assembly code:
a = b + c + d + e;

## Slide 5
Example
C code a = b + c + d + e;
translates into the following assembly code:
add a, b, c add a, b, c
add a, a, d or add f, d, e
add a, a, e add a, a, f
Instructions are simple: fixed number of operands (unlike C)
A single line of C code is converted into multiple lines of
assembly code
Some sequences are better than others… the second
sequence needs one more (temporary) variable f

## Slide 6
Subtract Example
C code f = (g + h) – (i + j);
Assembly code translation with only add and sub instructions:

## Slide 7
Subtract Example
C code f = (g + h) – (i + j);
translates into the following assembly code:
add t0, g, h add f, g, h
add t1, i, j or sub f, f, i
sub f, t0, t1 sub f, f, j
Each version may produce a different result because
floating-point operations are not necessarily
associative and commutative… more on this later

## Slide 8
Operands
In C, each “variable” is a location in memory
In hardware, each memory access is expensive – if
variable a is accessed repeatedly, it helps to bring the
variable into an on-chip scratchpad and operate on the
scratchpad (registers)
To simplify the instructions, we require that each
instruction (add, sub) only operate on registers
Note: the number of operands (variables) in a C program is
very large; the number of operands in assembly is fixed…
there can be only so many scratchpad registers

## Slide 9
Registers
The MIPS ISA has 32 registers (x86 has 8 registers) –
Why not more? Why not less?
Each register is 32-bit wide (modern 64-bit architectures
have 64-bit wide registers)
A 32-bit entity (4 bytes) is referred to as a word
To make the code more readable, registers are
partitioned as $s0-$s7 (C/Java variables), $t0-$t9
(temporary variables)…

## Slide 10
Memory Operands
Values must be fetched from memory before (add and sub)
instructions can operate on them
Load word
lw $t0, memory-address
Store word
sw $t0, memory-address
How is memory-address determined?
Register
Memory
Register
Memory

## Slide 11
Memory Address
The compiler organizes data in memory… it knows the
location of every variable (saved in a table)… it can fill
in the appropriate mem-address for load-store instructions
int a, b, c, d[10]
Memory
…
Base address

## Slide 12
Immediate Operands
An instruction may require a constant as input
An immediate instruction uses a constant number as one
of the inputs (instead of a register operand)
addi $s0, $zero, 1000 # the program has base address
# 1000 and this is saved in $s0
# $zero is a register that always
# equals zero
addi $s1, $s0, 0 # this is the address of variable a
addi $s2, $s0, 4 # this is the address of variable b
addi $s3, $s0, 8 # this is the address of variable c
addi $s4, $s0, 12 # this is the address of variable d[0]

## Slide 13
Memory Instruction Format
The format of a load instruction:
destination register
source address
lw $t0, 8($t3)
any register
a constant that is added to the register in brackets

## Slide 14
Example
Convert to assembly:
C code: d[3] = d[2] + a;

## Slide 15
Example
Convert to assembly:
C code: d[3] = d[2] + a;
Assembly: # addi instructions as before
lw $t0, 8($s4) # d[2] is brought into $t0
lw $t1, 0($s1) # a is brought into $t1
add $t0, $t0, $t1 # the sum is in $t0
sw $t0, 12($s4) # $t0 is stored into d[3]
Assembly version of the code continues to expand!

## Slide 16
Numeric Representations
Decimal 3510
Binary 001000112
Hexadecimal (compact representation)
0x 23 or 23hex
0-15 (decimal)  0-9, a-f (hex)

## Slide 17
Instruction Formats
Instructions are represented as 32-bit numbers (one word),
broken into 6 fields
R-type instruction add $t0, $s1, $s2
000000 10001 10010 01000 00000 100000
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
op rs rt rd shamt funct
opcode source source dest shift amt function
I-type instruction lw $t0, 32($s3)
6 bits 5 bits 5 bits 16 bits
opcode rs rt constant

## Slide 18
Logical Operations
Logical ops C operators Java operators MIPS instr
Shift Left << << sll
Shift Right >> >>> srl
Bit-by-bit AND & & and, andi
Bit-by-bit OR | | or, ori
Bit-by-bit NOT ~ ~ nor

## Slide 19
Control Instructions
Conditional branch: Jump to instruction L1 if register1
equals register2: beq register1, register2, L1
Similarly, bne and slt (set-on-less-than)
Unconditional branch:
j L1
jr $s0
Convert to assembly:
if (i == j)
f = g+h;
else
f = g-h;

## Slide 20
Control Instructions
Conditional branch: Jump to instruction L1 if register1
equals register2: beq register1, register2, L1
Similarly, bne and slt (set-on-less-than)
Unconditional branch:
j L1
jr $s0
Convert to assembly:
if (i == j) bne $s3, $s4, Else
f = g+h; add $s0, $s1, $s2
else j Exit
f = g-h; Else: sub $s0, $s1, $s2
Exit:

## Slide 21
Example
Convert to assembly:
while (save[i] == k)
i += 1;
i and k are in $s3 and $s5 and
base of array save[] is in $s6

## Slide 22
Example
Convert to assembly:
while (save[i] == k)
i += 1;
i and k are in $s3 and $s5 and
base of array save[] is in $s6
Loop: sll $t1, $s3, 2
add $t1, $t1, $s6
lw $t0, 0($t1)
bne $t0, $s5, Exit
addi $s3, $s3, 1
j Loop
Exit: